Equipment Program

Clinical Considerations for Prescribers
Bath Aids (including; Bath Benches, Bath Boards, Children’s Bath Aids, Swivel Bath Seat)

February  2013

Clinical Assessment

- Does the client have sufficient sitting balance to use prescribed aid?

- Is there sufficient flat bath surface to position most of the bench over the bath or bath aid flat on the bottom of the bath.

- Will there be enough space in front of item to provide room for client to lift legs into bath?

- Which side does the rail need to be to facilitate transfers – rail needs to be positioned nearest the wall.

- Check client weight

- Can the client transfer safely into the seat from outside the bath?

- Is the client or carer able to use all features of the aid appropriately?

- Bath boards need to have a minimum 20mm overlap with both edges of the bath – therefore are the flat edges of the bath wide enough?

- Does the client have the cognitive capacity to remember how to transfer on/ off safely?

Installation Considerations

- Must be installed by trained staff.

- Adjust legs of aid to make seat level.

- Check that once adjusted appropriately, the height is appropriate for safe transfers for the client.

- Do not leave out of position unless competent carer can demonstrate correct repositioning.

Client / Carer Instructions

- Demonstrate correct method of transfers

- Observe transfers with client on and off the item.

- Check item before each use to ensure that it is securely attached to bath and in appropriate location for facilitate safe transfers

- Explain that regular wiping of the item, particularly underneath will prolong it’s life.

- Ensure swivel action of swivel chair is explained to client, in particular the locking lever.

- Inform client / carer to check monthly for rust at rivets and welds and for general deterioration.

- Inform the client / carer that if any bath aid is removed from the bath, it needs to be securely repositioned again before use.

- Ensure parental/carer supervision at all times when children’s bath aid in use.

Safety and Review  considerations

Review – 12 monthly, as standard.  Review more frequently if client is heavy or transfers awkwardly.

Checklist

- That bath bench is still in use and appropriate for the client’s needs.

- Check transfers in and out of the bath

- Check client’s weight and whether equipment item is still appropriate

- Check height adjustments are working and that pins fully protrude through holes

- Check rivets and other joins for rust and stability

- Check for any surface deterioration to the seating